## Slide 1: Secure IoT solution for office building monitoring

## Slide 2: Purpose of the thesis
Designing a low-powered IoT solution which enforces entity attestation and securely transmits data into the cloud, performing edge Machine Learning and issuing blockchain transactions.

## Slide 3: Contents
Introduction
Architecture Overview
Design of the IoT Node
Cloud-Hosted Microservices
Securing the Solution – Attestation Service
Securing the Solution – Protecting Secrets
Conclusion

## Slide 4: INTRODUCTION
Current IoT fog computing solutions pose a severe security risk by introducing single points of failure
Creating an architecture that is more resilient is imperative in mission-critical applications

## Slide 5: Architecture overview
Wi-Fi enabled IoT nodes are pushing sensitive data into the cloud
Fast dispatch and reaction is achieved through encoding of the payload to reduce size
Complete confidentiality is achieved through End-to-End encryption
Each entity is attested

## Slide 6: Design of the IoT node
Built using off the shelf components:
  Espressif ESP32
  DHT11 Temperature and Humidity Sensor
  SW-420 Vibration Sensor
  MQ-2 Gas Sensor
Performs Edge Machine Learning
Issues blockchain transactions
Runs ESP-IDF and uses a CMake derived build system
Has two Xtensa LX6 CPU cores and supports FreeRTOS
Baked-in support for mbedTLS, which offers a plethora of cryptographic operations
Sensor data is sent CBOR encoded and formatted according to the IPSO guidelines

## Slide 7: Cloud-Hosted Microservices
Hosted on an Oracle Cloud Instance with 4 ARM cores and 24 GB of RAM
Developed in Spring Boot
Conforms to the microservice architecture: exposes all available endpoints through a web-facing gateway
Runtime serving of configuration files using Spring Cloud Configuration Server
Service Discovery through Netflix Eureka Server
Transport layer security through HTTPS
All requests are authenticated using JWT
Deployed using Docker Compose

## Slide 8: Securing the solution Attestation Service
01
Through signed X.509 certificates
02
Through EC Ephemeral Diffie-Hellman
03
By calling the DB microservice
04
Using the established key for TLS-PSK
Mutual Authentication
Session Key Establishment
Instance ID allocation
MQTT Connection

## Slide 9: Securing the Solution Protecting Secrets
Credentials and other sensitive information are served to the microservices using HashiCorp Vault over HTTPS
The chosen strategy to prevent the secret zero problem is cubbyhole response wrapping
The flash storage of the IoT node is encrypted, saving the key in eFUSE

## Slide 10: Conclusion
Resilient and secure solution
End-to-End encryption
Resiliency is improved by removing gateways
Entity attestation is enforced
Securing the Solution Protecting Secrets

## Slide 11: Conclusion
Feature rich and easily expandable
Handles sensor data transparently which allows facile extensions
Performs edge Machine Learning supporting a large number of models
Able to issue blockchain transaction
  Persisting records into Ethereum Smart Contracts
Securing the Solution Protecting Secrets

## Slide 12: Conclusion
Interoperable
Industry standards such as IPSO formatting guide and CBOR have been used
Transport over IP
Securing the Solution Protecting Secrets

## Slide 13: THANK YOU!